## Slide 1: Robot Modelling
Mini challenge 1

## Slide 2: Introduction
Introduction
This mini challenge is intended for the student to review the concepts introduced in the previous sessions.
The activity consists of modelling a differential drive robot in RVIZ.
The robot must be modelled using only ROS markers.
The robot must be modelled using the tf2 library of ROS.
Mini-challenge

## Slide 3: Robot modelling
Make a new package called “simple_mobile_robot”, with the following packages
  rospy, std_msgs, tf2_ros, visualization_msgs tf_conversions, geometry_msgs
Use transformations and different markers to build a simple mobile robot (differential drive).
  The robot must contain a chassis, two wheels and a caster ball.
  The student must use various shapes of markers to create their optimal robot.
Front View
Back View

## Slide 4: Robot modelling
The expected transformations are represented on the right diagram.
world: fixed frame
base_link: robot pose representation in the 2D (x,y plane).
chassis: link representing the chassis centre.
wheel_r, wheel_l: wheel link
caster: caster ball link.
world
base_link
chassis
wheel_r
wheel_l
caster
dynamic tf
static tf
dynamic tf
static tf
dynamic tf

## Slide 5: Robot modelling
Side View

## Slide 6: Expected results
The robot should spawn in the RVIZ world.
The robot should be able to move around a central position.
If possible, move the wheels.