## Slide 1: Puzzlebot Gazebo Simulator
Instructions manual

## Slide 2: Gazebo simulation
Initialising the simulation
Download the ROS packages to your workspace source folder (e.g., catkin_ws/src)
Build and source the packages
Run the Puzzlebot gazebo simulator using the following command
The following screen should appear
  puzzlebot_gazebo
  puzzlebot_control
  puzzlebot_description
  $ cd ~/catkin_ws/
  $ catkin_make
  $ source devel/setup.bash
  $ roslaunch puzzlebot_gazebo puzzlebot_gazebo.launch

## Slide 3: Gazebo simulation
Initialising the simulation
Open another terminal
Verify the topics generated by the simulator using the following command
The following list of topics should appear
  $ rostopic list

## Slide 4: Gazebo simulation
Running the simulation
Sending velocity commands to the robot is done using the following topic
  /puzzlebot_1/base_controller/cmd_vel
  Topic: /puzzlebot_1/base_controller/cmd_vel
  Message: geometry_msgs/Twist
    "linear:
    x: linear_velocity (v)
    y: 0.0
    z: 0.0
    angular:
    x: 0.0
    y: 0.0
    z: angular_velocity (omega)"
The message to be used is a geometry_msg/Twist (more information here)
The robot’s linear velocity and angular velocity must be set in the linear.x and angular.z sections of the message (ROS convention for differential drive robots).

## Slide 5: Gazebo simulation
Running the simulation
To publish a message to the gazebo-simulated robot from the terminal can be done as follows.
The previous command will make the robot to run in a circle.
  $ rostopic pub -r 10 /puzzlebot_1/base_controller/cmd_vel geometry_msgs/Twist "linear:
  x: 0.3
  y: 0.0
  z: 0.0
  angular:
  x: 0.0
  y: 0.0
  z: 0.3"

## Slide 6: Gazebo simulation
Running the simulation
To obtain the wheel speed () from the robot, the following topics must be used
Getting the wheel velocities from the robot is done using the following command
The topic uses a std_msg/Float32 message.
  /puzzlebot_1/wr
  /puzzlebot_1/wl
  $ rostopic echo /puzzlebot_1/wl
  Topic: /puzzlebot_1/wl
  Message: std_msgs/Float32

## Slide 7: Robot Teleoperation
Install the teleoperation package
Run the gazebo simulator as described before
In another terminal, run the teleoperation node as follows
Control the robot using the keyboard (i, j, l, k) as described on the terminal.
  rosrun teleop_twist_keyboard teleop_twist_keyboard.py _repeat_rate:=10 cmd_vel:=puzzlebot_1/base_controller/cmd_vel _speed:=0.4 _turn:=1.1
  sudo apt install ros-noetic-teleop-twist-keyboard
  $ roslaunch puzzlebot_gazebo puzzlebot_gazebo.launch