## Slide 1: Activity
Motor Dynamical Simulation

## Slide 2: Activity
Introduction
In this activity, the student will learn how to simulate a DC motor using its dynamical model and visualise the model’s output in RVIZ.
The node: “motor_sim” will be developed.
“motor_sim” Node: Simulate a DC motor using its dynamical model. The input to the model is the voltage (), and the output is the angular velocity of the motor ().

## Slide 3: Motor Simulation in RVIZ
Download the package called “motor_sim”, from the folder “/Week4/Activity1/” to your “catkin_ws”
Create a node called “motor_sim.py”” inside the scripts folder
  cd ~/catkin_ws/src/motor_sim/scripts/
  touch motor_sim.py
Do not forget to give executable permission to the file
cd ~/catkin_ws/src/motor_sim/scripts/
sudo chmod +x motor_sim.py
Modify the CMake file to include the newly created node to the
catkin_install_python(PROGRAMS scripts/motor_sim.py
DESTINATION ${CATKIN_PACKAGE_BIN_DESTINATION})

## Slide 4: Motor Simulation in RVIZ
Open the file motor_sim.py
Simulate the dynamics of a DC motor, using the DC motor dynamical model.
where: is the moment of inertia of the rotor, is the damping ration of the mechanical system, is the electric resistance, is the electric inductance, and are the electromotive force constants, is the load, is the source voltage (or the input), is the rotating speed (the output).
#Motor Parameters
R = 6.0
L = 0.3
k1 = 0.04
k2 = k1
J = 0.00008
b = 0.00025
m = 0.0
#Motor governing equation
current_dot = -(R/L)*current-(k1/L)*omega+(1/L)*(u)
current += current_dot*dt
omega_dot = (k2/J)*current-(b/J)*omega-(1/J)*m
omega += omega_dot*dt

## Slide 5: Motor Simulation in RVIZ
Subscribe the model to the topic “/motor_input” and publish the model’s output in the topic “/motor_output”.
  Both messages can be Float32 messages.
Make sure to add print some values to verify the program is working properly (debug).
Compile the program
cd ~/catkin_ws
catkin_make
Start ROS
roscore
Run the node
rosrun motor_sim motor_sim.py
Open the rqt_plot to verify the results
Publish a value in the “/motor_input” topic in the range of .
  rostopic pub /motor_input std_msgs/Float32 "data: 0.3"
Verify the results

## Slide 6: Activity
Part 2: Visualisation

## Slide 7: Motor Simulation in RVIZ
Use the “motor_JointPub.py” to publish the data to the joints of the model.
Add the newly created node “motor_sim.py” to the launch file “motor_sim.launch”.
<?xml version="1.0"?>
<launch>
<!-- Load URDF-->
<arg name="motor_urdf" default="$(find links_act)/urdf/dc_motor.urdf"/>
<!--Set URDF file as a robot_description parameter-->
<param name="robot_description" command="cat $(arg motor_urdf)" />
<!--Initialise robot_state_publisher-->
<node pkg="robot_state_publisher" type="robot_state_publisher" name="motor_urdf_pub" >
</node>
<!--Initialise motor joint publisher-->
<node pkg="motor_sim" type="motor_JointPub.py" name="motor_JointPub" />
<!--Initialise motor dynamical simulation-->
<node pkg="motor_sim" type="motor_sim.py" name="motor_Sim" />
</launch>

## Slide 8: Motor Simulation in RVIZ