## Slide 1: Activity
Single Link Manipulator Simulation

## Slide 2: Activity
Introduction
In this activity, the student will learn how to simulate a single link manipulator dynamics using the governing equations derived from the Euler-Lagrange methodology.

## Slide 3: SLM Simulation in RVIZ
Download the package “slm_sim”, from GitHub “Week4/Activities/Activity 2” to your “catkin_ws”
Create a node called slm_sim.py inside the scripts folder
  cd ~/catkin_ws/src/slm_sim/scripts/
  touch scripts/slm_sim.py
Give executable permission to the file
cd ~/catkin_ws/src/slm_sim/scripts/
sudo chmod +x slm_sim.py
Modify the CMake file to include the newly created node in the
catkin_install_python(PROGRAMS scripts/slm_sim.py
DESTINATION ${CATKIN_PACKAGE_BIN_DESTINATION})

## Slide 4: SLM Simulation in RVIZ
Open the file slm_sim.py
Simulate the dynamics of a single link manipulator using the following dynamical model.
Let and
where: link has inertia and the centre of mass, , is located at , a distance from the origin (point of rotation), and is the friction coefficient.
** For this case since it is a uniform rod, the centre of mass is located at the centre of the rod, then:

## Slide 5: SLM Simulation in RVIZ
#SLM Parameters
k = 0.01
m = 0.75
l = 0.36
g = 9.8
Tau = 0.0
x1 = 0.0
x2 = 0.0
#SLM governing equation
x1 += x2*dt
x2_dot = (1/(J+ma^2)) * (- mga cos(x1) – kx2 + Tau)
x2 += x2_dot*dt
SLM Manipulator
/tau
/joint_states

## Slide 6: SLM Simulation in RVIZ
Subscribe the model to the topic “/tau” and publish the model’s output in the topic “/joint_states”.
Make sure to add print some values to verify the program is working properly (debug).
Compile the program
cd ~/catkin_ws
catkin_make
Launch the node from the launch file
roslaunch slm_sim pendulum_sim.launch
Open rviz and rqt_plot to verify the results
rosrun rqt_plot rqt_plot
rqt_multiplot can be installed to view the phase diagram
sudo apt install ros-noetic-rqt-multiplot
rosrun rqt_multiplot rqt_multiplot